## Slide 1: Gears, Pulley Drives, and Sprockets

## Slide 2: Gears, Pulleys, & Sprockets
Mechanisms used to transfer energy through rotary motion.
Change the speed of rotation
Change the direction of rotation
Change the amount of torque available to do work

## Slide 3: Gears
A gear train is made when two or more gears are meshed
A gear train is a mechanism used for transmitting rotary motion and torque through interlocking teeth.
Driver gear causes motion
Motion is transferred to the driven gear

## Slide 4: Gears
Mating gears always turn in opposite directions.
An Idler Gear allows the driver and driven gears to rotate in the same direction.
Mating gears always have the same size teeth (diametric pitch).

## Slide 5: Gears
The rpm of the larger gear is always slower than the rpm of the smaller gear.
Gears locked together on the same shaft will always turn in the same direction and at the same rpm.

## Slide 6: Gear Ratios
6
2in.
40rpm
40 ft-lb
12
4in.
20rpm
80 ft-lb
Variables to know
n = number of teeth
d = diameter
ω = angular velocity (speed)
τ = torque
** Subscripts in and out are used to distinguish between gears **
4”
nin= | nout =
din = | dout =
ωin = | ωout =
τin = | τout =
Notes: In order to effectively work among the ratios, you must be able to distinguish the following symbols.
The symbol for angular velocity is the Greek lower case Omega.
The symbol for torque is the Greek lower case Tau.
The subscript “in” and “out” simply identify whether or not the characteristic of the gear refers to the input or output gear.
Note the rotation direction of the gears.

## Slide 7
Gear Ratios
Equations to know
GR = Gear Ratio
GR = MA

## Slide 8
Gear Ratios
What is the gear ratio between gear A and B?
What is the gear ratio between gear B and C?
What is the gear ratio between gear C and D?

## Slide 9
Gear Ratios
What is the TOTAL gear train gear ratio?
What would the total gear ratio be if the last gear had 40 teeth?
If gear A and D were directly connected to each other, what would the resulting gear ratio be?
or

## Slide 10
Compound Gear Train
The two middle gears share a common axle, so they rotate at the same speed.
This allows the final gear to rotate slower and produce more torque than if it were connected only to the driver gear.
Driver
Notes: A simple method to gain torque would be to turn the final gear that was added into the driver gear.

## Slide 11
Compound Gear Ratios
50 T
40 T
20 T
10 T
A
B
C
D
What is the gear ratio between gear A and B?
What is the gear ratio between gear C and D?
What is the gear ratio of the entire gear train?

## Slide 12: Pulley and Belt Systems
Equations
d = diameter ω = angular velocity (speed) τ = torque
out
in
2in.
Notes: The belt is a continuous band that wraps around the pulleys to transmit power. The ratios are the same as for gears. The only exception is that there are no teeth to count.
Another difference is that two pulleys connected by a belt will rotate in the same direction.

## Slide 13: Sprocket and Chain Systems
n = number of teeth d = diameter ω = angular velocity (speed) τ = torque
3in.
out
1.5in.
in
90rpm
45rpm
60 ft-lb
120 ft-lb
Notes: Sprockets and gears are often confused. Gears mesh with gears, while sprockets use chains to transfer power between sprockets.

## Slide 14: Comparing Pulleys and Sprockets
 | Pulley | Sprocket
Method of Transmitting Force | Belt | Chain
Advantages | Quiet, no lubrication needed, inexpensive | No slip, greater strength
Disadvantages | Can slip | Higher cost, needs lubrication, noisy

## Slide 15: Image Resources
Microsoft, Inc. (2008). Clip art. Retrieved January 15, 2008, from http://office.microsoft.com/en-us/clipart/default.aspx