## Slide 1: Mechanisms Simple Machines
Lever, Wheel and Axle, & Pulley

## Slide 2: Simple Machines
The Six Simple Machines
Mechanisms that manipulate magnitude of force and distance.
Lever
Wheel and Axle
Pulley

## Slide 3: The Six Simple Machines
Inclined Plane
Screw
Wedge

## Slide 4: Mechanical Advantage
Ratio of the magnitude of the resistance and effort forces
Ratio of distance traveled by the effort and the resistance force
Calculated ratios allow designers to manipulate speed, distance, force, and function

## Slide 5: Mechanical Advantage Example
Effort force travels 4 times greater distance than the resistance force.
Magnitude of Force:
Distance Traveled by Forces:
A mechanical advantage of 4:1 tells us
what about a mechanism?
Effort force magnitude is 4 times less than the magnitude of the resistance force.

## Slide 6: Work
The force applied on an object times the distance traveled by the object
Initial position
Final position
Distance (d)
Force (F)
Work = Force * Distance = F*d
*The force needed to overcome friction is not considered*

## Slide 7: Work
The product of the effort times the distance traveled will be the same regardless of the system mechanical advantage

## Slide 8: Mechanical Advantage Ratios
One is the magic number
If MA is greater than 1:
Proportionally less effort force is required to overcome the resistance force
Proportionally greater effort distance is required to overcome the resistance force
If MA is less than 1:
Proportionally greater effort force is required to overcome the resistance force
Proportionally less effort distance is required to overcome the resistance force
MA can never be less than or equal to zero.

## Slide 9: Ideal Mechanical Advantage (IMA)
Theory-based calculation
Friction loss is not taken into consideration
Ratio of distance traveled by effort and resistance force
Used in efficiency and safety factor design calculations
DR = Distance traveled by resistance force
DE = Distance traveled by effort force

## Slide 10: Actual Mechanical Advantage (AMA)
Inquiry-based calculation
Frictional losses are taken into consideration
Used in efficiency calculations
Ratio of force magnitudes
FE = Magnitude of effort force
FR = Magnitude of resistance force

## Slide 11
Can you think of a machine that has a mechanical advantage greater than 1?
Real World Mechanical Advantage

## Slide 12
Can you think of a machine that has a mechanical advantage less than 1?
Real World Mechanical Advantage

## Slide 13: Lever
A rigid bar used to exert a pressure or sustain a weight at one point of its length by the application of a force at a second and turning at a third on a fulcrum.

## Slide 14: 1st Class Lever
Fulcrum is located between the effort and the resistance force
Effort and resistance forces are applied to the lever arm in the same direction
Only class of lever that can have a MA greater than or less than 1
MA =1
Effort
Resistance
Resistance
Effort
MA <1
Effort
Resistance
MA >1

## Slide 15: 2nd Class Lever
Fulcrum is located at one end of the lever
Resistance force is located between the fulcrum and the effort force
Resistance force and effort force are in opposing directions
Always has a mechanical advantage >1
Resistance
Effort

## Slide 16: 3rd Class Lever
Fulcrum is located at one end of the lever
Effort force is located between the fulcrum and the resistance
Resistance force and effort force are in opposing directions
Always has a mechanical advantage < 1
Resistance
Effort

## Slide 17: Moment
The turning effect of a force about a point equal to the magnitude of the force times the perpendicular distance from the point to the line of action from the force.
Moment = Force x Distance
Torque: A force that produces or tends to produce rotation or torsion.

## Slide 18: Lever Moment Calculation
15 lbs
Moment =
Force x Distance
5.5 in.
Resistance
Effort
Calculate the effort moment acting on the lever above.
Effort Moment =
Effort Moment =
15 lb x 5.5 in.
82.5 in. lb
15 lb

## Slide 19: Lever Moment Calculation
When the effort and resistance moments are equal, the lever is in static equilibrium.
Static equilibrium:
A condition where there are no net external forces acting upon a particle or rigid body and the body remains at rest or continues at a constant velocity.

## Slide 20: Lever Moment Calculation
Resistance
15 lbs
82.5 in.-lb = 36 2/3 lb x DR
Using what you know regarding static equilibrium, calculate the unknown distance from the fulcrum to the resistance force.
Static equilibrium:
Effort Moment = Resistance Moment
5.5 in.
?
15 lb
36 2/3 lb
Effort
82.5 in.-lb /36.66 lb = DR
DR = 2.25 in.

## Slide 21: Lever IMA
Effort
Resistance
DE = 2 π (effort arm length)
Both effort and resistance forces will travel in a circle if unopposed.
Circumference is the distance around the perimeter of a circle.
Circumference = 2 π r
DR = 2 π (resistance arm length)
______________________
IMA =
2 π (effort arm length)
2 π (resistance arm length)

## Slide 22: Lever AMA
The ratio of applied resistance force to applied effort force
5.5 in.
2.25 in.
16 lb
32 lb
Effort
Resistance
What is the AMA of the lever above?
AMA = 2:1
What is the IMA of the lever above?
IMA = 2.44:1
Why is the IMA larger than the AMA?

## Slide 23: Efficiency
In a machine, the ratio of useful energy output to the total energy input, or the percentage of the work input that is converted to work output
The ratio of AMA to IMA
What is the efficiency of the lever on the previous slide? Click to return to previous slide
No machine is 100% efficient.
AMA = 2:1
IMA = 2.44:1
Efficiency
= .82 or 82.00%

## Slide 24: Wheel & Axle
A wheel is a lever arm that is fixed to a shaft, which is called an axle.
The wheel and axle move together as a simple lever to lift or to move an item by rolling.
It is important to know within the wheel and axle system which is applying the effort and resistance force – the wheel or the axle.
Can you think of an example of a wheel driving an axle?

## Slide 25: Wheel & Axle IMA
DE = π [Diameter of effort (wheel or axle)]
Both effort and resistance forces will travel in a circle if unopposed.
Circumference = 2 π r or π d
DR = π [Diameter resistance (wheel or axle)]
______________________
IMA =
π (effort diameter)
π (resistance diameter)
What is the IMA of the wheel above if the axle is driving the wheel?
What is the IMA of the wheel above if the wheel is driving the axle?
6 in. / 20 in. = .3 = .3:1 = 3:10
20 in. / 6 in. = 3.33 = 3.33:1
Ǿ6 in.
Ǿ20 in.

## Slide 26: Wheel & Axle AMA
Ǿ6 in.
Ǿ20 in.
200lb
70lb
What is the AMA if the wheel is driving the axle?
Use the wheel and axle assembly illustration to the right to solve the following.
200lb/70lb = 2.86 = 2.86:1
What is the efficiency of the wheel and axle assembly?
2.86/3.33 = .859 or 85.9%

## Slide 27: Pulley
A pulley is a lever consisting of a wheel with a groove in its rim which is used to change the direction and magnitude of a force exerted by a rope or cable.

## Slide 28: Pulley IMA
Fixed Pulley
- 1st class lever with an IMA of 1
- Changes the direction of force
10 lb
5 lb
5 lb
Movable Pulley
- 2nd class lever with an IMA of 2
- Force directions stay constant
10 lb
10 lb

## Slide 29: Pulleys In Combination
Fixed and movable pulleys in combination provide mechanical advantage and a change of direction for effort force.
What is the IMA of the pulley system on the right?
800 lb
Movable pulleys in combination provide mechanical advantage without change in effort force direction.
40 lb
40 lb
20 lb
20 lb
10 lb
10 lb
What is the IMA of the pulley system on the left?
4
8
80 lb

## Slide 30: Pulley AMA
What is the AMA of the pulley system on the right?
800 lb
230 lb
AMA = 3.48 = 3.48:1
What is the efficiency of the pulley system on the right?
Efficiency =
= .87 or 87%

## Slide 31
2nd Class lever
MA = 2
1st Class lever
MA = 1
A
B
C
D
Pulleys in combination or Block and tackle are a compound machine.
Calculating mechanical advantage
MAT = MAA * MAB * MAC * MAD
MAT = 1 * 1 * 2 * 2
MAT = 4

## Slide 32: Image Resources
Microsoft, Inc. (2008). Clip art. Retrieved January 10, 2008, from http://office.microsoft.com/en-us/clipart/default.aspx